Residential Rental and Resale Inspection Checklist

- Smoke detectors are required on all levels, including attic spaces/ storage area.  Smoke detectors shall be installed within 10 feet of sleeping areas.  Carbon monoxide detectors must be installed in the vicinity of each sleeping area.

- Holes in walls, floors and ceilings shall be repaired.

- Hot & cold water in kitchens and bathrooms shall operate properly and have shut off valves for each. All sinks shall have approved drain traps.

- Toilets shall be secured, operate properly and have a shut off valve on the water feed line.

- All stoves must have an anti tipping device.

- Electrical outlets shall be in good working order. Junction boxes shall have proper cover plates. All wire connections shall be boxed, wire nutted with cover plate installed.

- Water heater & boilers shall be in good working order.  Adequate ventilation is required to assure proper combustion.  Vent/flue pipes to be properly sealed at chimney connection.  Screws and supports on vent pipe if needed.

- Main electrical services line (pipe or cable) shall be properly secured to the structure with approved cable straps or pipe straps.

- Fire places/wood stove shall be properly maintained and in good condition. (if applicable).

- All doors shall have proper hardware.  Double keyed deadbolt locks are not permitted on exit doors.

- All residential properties must have operable kitchens and bathroom in each apartment.

- Every window (other than fixed windows) shall operate properly, repair all broken windowpanes.  Window screens shall be free from holes, rips and tears.

- Roof gutters and leaders must be properly installed and in good repair.  Roof shall be in good repair with no evidence of leaks.  Foundation walls shall be in good repair.

- The use of extension cords to replace permanent wiring is not permitted and is illegal.  Garage door openers shall be plugged directly into a power supply without the use of an extension cord.

- Any open permits must be finalized before a CO can be issued.

- House numbers shall be 4” minimum height, mounted so as to be visible from curb line.

- Handrails are required on all stairways and steps with three or more risers.  All stairways shall be in good condition.

- Yard area: grass must be cut and trimmed; weeds must be cut and removed.  Premises shall be free of rodents, insects and offensive odors.

- Swimming pool protection (if applicable).